MACH4METAL

metalworking machinery

DARLEY Pressbrake 4300 x 150 T

- Merk		: Darley Holland

- Type		: EHP 150 43/37

- Serial 	: 12.1607

- YOP		: 1993

- Max. bending length	: 4.300

- Between column		: 3.700

- Max. force Kn		:   150

- Troath			: 300

- Max. stroke			: 175

- Die height			: 400

- Approch speed	:  80 mm/sec.

- Pressing speed	:    8 mm/sec.

- Return speed	:  70 mm/sec.

- CNC Delem DA 23

- Y1/Y2/X/V-Crowning

- Hydraulic upper clamping

- 2 Heavy duty sheet arms (hand)

- Power          :     11 kW

- Length	:   4.420

- Width	:   1.680

- Height	:   2.935

- Weight 	: 16.000

- Tooling package upper & lower

- Good running condition

Please Note: The above information has been obtained to the best of our ability and belief from, and from the manufacturers where possible. It is given in good faith, but its accuracy can not be guaranteed. Accordingly, it will not form a representation or constitute contractual terms. We advise you to check any vital details!

# Text boxes

Transito 21

6909 DA BABBERICH Netherlands

Tel. +31 (0)316-247123

Fax: +31 (0)316-247956

info@mach4metal.com

www.mach4metal.com

Bank No : 66.52.13.883

IBAN    : NL33 INGB 0665 2138 83

BIC      : INGBNL2A