MACH4METAL

metalworking machinery

CNC Berthiez vertical borer

- Make		: Berthiez France

- Typ		: TFM 160

- Age		: 78 / Retrofitted 1997

- Serial. No	: 133196

- Chuck Ø		          	:   1.650

- Max swing Ø			:   1.880

- Max. turning  height		:   1.600

- Work pieces weight		: 15.000

- Chuck speeds	Rpm		: 2 – 250

- Vert. Travel support		:   1.300

- Power main motor KW		:      45

- Ram travel			:  1.000

- Feed rate			: 360 mm/Rev

- Rapid feed			: 6.000 mm/M

- Dimension

- Length		:   7.500

- Width		:   5.480

- Height		:   5.100

- Weight		: 18.000

- ATC 12 position tool changer

- Fanuc OTS CNC in 2 axis

- Chip conveyor

- 4 heavy jaws

Please Note: The above information has been obtained to the best of our ability and belief from, and from the manufacturers where possible. It is given in good faith, but its accuracy can not be guaranteed. Accordingly, it will not form a representation or constitute contractual terms. We advise you to check any vital details

# Text boxes

Transito 21,

6909 DA BABBERICH, Netherlands

Tel. + 31 (0)316 – 247123

Fax. + 31 (0)316 - 247956

info@mach4metal.com

www.mach4metal.com

Bank No : 66.52.13.883

IBAN    : NL33 INGB 0665 2138 83

BIC      : INGBNL2A