STOCK No F2628

SPECIFICATION

SWEENEY & BLOCKSIDGE TYPE P50 MECHANICAL POWER PRESS

TYPE: 	P50

SERIAL No: 	8369

MFD Aug: 	1995

Bottom Bolster: 			630 x 750mm

Hole Bottom Bolster:			130 x 300mm

Ram Bolster: 				90 x 260mm

Max Adjustable Ram Stroke:	 	100mm

Window Aperture: 			760 x 250

Side Window Aperture: 		215 x 250mm

Main Motor: 				5.5Kw

Electrics:				415v, 3ph, 50 Cycles

Complete with:

Single Stroke

Continuous Stroke

Barring

Piece Counter

Pneumatic Clutch

Pendant Control

Interlocked Guards

,

Approximate Dimensions: 	1400 x 1500 x 2330mm

Approximate Weight: 		3000Kg