MACH4METAL

metalworking machinery

TOS lathe SUA 150 x 12.000 mm

- Make		: TOS Celakovice

- Type		: SU 150 H / 12.000

- Age		: 2004

- Serial		: 72 529

- Max. turning Ø bed	     :  1.500

- Max. turning Ø carriage       :  1.200

- Centre height	               :    625

- Centre distance		     : 12 Mtr

- Work load supported	     : 8.000

- Work load between centre   : 6.000

- Bed width			     :    800

- Bed height			     :    630

- Spindle bore		     :    128

- Speeds 4 ranges 		     :    630

- Pinole	Ø			     :    150

- Stroke pinole	               :   200

- Feed rate			: 1.000 mm/M

- Rapid feed			: 5.000 mm/M

- Dimensions:

- Length	: 17.200

- Width	: 3.185

- Height	: 2.200

- Weight        : 16.000 Kg

- Power		: 37 kW

- Motorised tailstock

- CE safety guides / covers

Please Note: The above information has been obtained to the best of our ability and belief from, and from the manufacturers where possible. It is given in good faith, but its accuracy can not be guaranteed. Accordingly, it will not form a representation or constitute contractual terms. We advise you to check any vital details!

# Text boxes

Transito 21,

6909 DA BABBERICH, Netherlands

Tel. + 31 (0)316 – 247123

Bank No : 66.52.13.883

IBAN    : NL33 INGB 0665 2138 83

BIC      : INGBNL2A