Stock No: F3393

SPECIFICATION

GLEASON 645 G PLETE HYPOID SPIRAL BEVEL GEAR GENERATOR

Serial No:	770502

Model:	645 G Plete

MFD:	1980

Capacities:

Extreme Ratios			10:1

Root Angle Range:		-8° to 90°

Gear Diameter Maximum:

Outer Cone		Spiral		Cutter

Distance		Angle		Diameter

361.2mm		29.75°	304.8mm

356.9mm		30°		406.4mm

378mm		35°		457.2mm

Maximum Radial Settings:						266.7mm

Pitch Coarsest:							1.5 DP / 16.9 MOD

Face Width Maximum:						116.8mm

Full Depth:								31.8mm

Index Range:								5 – 80 Inclusive

Work Spindle:

Diameter of Taper Hole At Large End:				152.4mm

Taper Per Foot:							19.05mm

Depth of Taper:							152.4mm

Diameter of Hole Through Spindle:					127mm

Cutter Diameters:							9, 12, 16, 18”

Work Head Settings:

Offset Above Centre Maximum					114.3mm

Offset Below Centre Maximum:					114.3mm

Machine Centre to Nose of Spindle Maximum:			596.9mm

Cutter Speeds:							           19 – 167 Rpm Stepless

Feeds Infinitely Variable Per Tooth:					7 Seconds Minimum

Electrics:	415v, 3ph, 50 Cycles

Cutter Motor:	15 Hp

Approximate Dimensions:	3556 x 2032 x 2100mm

Approximate Weight:	26,490kg

Price………...£			Plus VAT (if applicable)

# OFFERED SUBJECT TO REMAINING UNSOLD

The above information is, to the best our knowledge correct, but purchasers are advised to check relevant details.