Stock No: F3025

SPECIFICATION

NIAGARA 200 TON MECHANICAL PRESS

Model BP2-200-72-36

Serial No 51265

Capacity:

Maximum Pressure:		200 tons

Maximum Stroke:		150mm

Shut Height:			635mm

Bottom Bolster:		1828 x 915mm

Top Bolster:			1828 x 915mm

Bolster Thickness:		178mm

Strokes per Min:		41 – 83

Side Window Aperture:

Front to Back:			558mm

Left to Right:			635mm

Complete With

Atkins Straightener,

Model: W6454

MFD: 2000

Serial No: RF127-450

Capacity 450mm x 6mm thick

134 Ft per Min

Sesco Detroit Michigan Leveler

Model 12-1019

Serial No: 19993-1

Maximum Coil Weight 15,000 lbs

Stock Width:	 1” – 24”

Tipped rate 140 ft. per min.

US gauge minimum 0.020 – maximum .200

Sesco Decoiler

Model: 55/553

Serial No:	 19992-1,

Maximum Coil Weight 15,000 lbs.

1” – 24” coil width,

Output rate 140 ft. per min.

US gauge min.020 – max.  .2,

Adjustable Material Conveyor

Coil Car

Parts Catcher & Scrap Conveyor

Price………...£			Plus VAT (if applicable)

# OFFERED SUBJECT TO REMAINING UNSOLD

The above information is, to the best our knowledge correct, but purchasers are advised to check relevant details.