STOCK NO: F3580

# SPECIFICATION

COLCHESTER MAGNUM 1250GAP BED CENTRE LATHE

TYPE:               	MAGNUM 1250

SERIAL NO:	9/0006B/00042

Capacities:

Swing Over Bed:				635mm

Swing Over Cross Slide:        			390mm

Swing In Gap:					900 x 300mm

Max Distance Between Centres:		3000mm

Spindle Bore:					118mm

Spindle Speeds:    				6.3 – 1250rpm

Feeds:	Sliding:				0.35 – 3.2mm per rev

Surfacing:			0.175 – 1.6mm per rev

Screw cutting:

TPI    						¼ - 120

METRIC					0.2 – 112mm pitch

MOD      					0.3 - 24

D.P  						1 - 60

Taper in tailstock:   				6MT

Motor:						15kw

Electrics:					414v, 3ph, 50 Cycles

Complete With:

380mm 3 Jaw Chuck

2 Axis DRO

2 No Feed Shaft Supports

Quick Change Tool Post & 3 Tool Holders

Lovo Light, Coolant

Chuck & Rear Splash Guard

Approximate Dimensions:		4900 x 1500 x 1900mm

Approximate Weight:	        		4500kg

Price………...£			Plus VAT (if applicable)

# OFFERED SUBJECT TO REMAINING UNSOLD

The above information is, to the best our knowledge correct, but purchasers are advised to check relevant details.