MACH4METAL

metalworking machinery

4 ROLL PLATE BENDER

HAEUSLER 3000 X 60 mm

- Make		: Haeusler Swiss

- Typ		: VRM HY

- Serial	 No	: WO 991 - 1833

- Age		: 2000 / 08

- Rolling width	: 3.000

- Rolling thickness   : 60 mm x R 2500

- Pre bending 	          : 45 mm x R 2500

- Top roll     Ø	:  560

- Side roll   Ø		:  400

- Lower roll Ø		:  540

- Rolling speed	   : 2 + 4 M/min

- Power 		   : 55.5 kW

- Adjustment top roll  : 0 – 200 mm/Min

- Adjustment side roll : 0 – 500 mm/Min

- Top support load ….

- Side support load…

- Length	:     6.670

- Width	:     2.900

- Height	:     3.075

- Weight	:  40.000 KG

- Conical bending

- Oil cooler

Please Note: The above information has been obtained to the best of our ability and belief from, and from the manufacturers where possible. It is given in good faith, but its accuracy can not be guaranteed. Accordingly, it will not form a representation or constitute contractual terms. We advise you to check any vital details!

# Text boxes

Transito 21

6909 DA BABBERICH Netherlands

Tel. +31 (0)316-247123

Fax: +31 (0)316-247956

info@mach4metal.com

www.mach4metal.com

Bank No : 66.52.13.883

IBAN    : NL33 INGB 0665 2138 83

BIC      : INGBNL2A