MACH4METAL

metalworking machinery

LEIFELD Spinning PLB 1800

- Make		: Leifeld Germany

- Typ		: Leico PLB 1800

- Age		: 1974

- No		: 8120

- Centre height above gap		:  2.300

- Centre height above lower bed :  1.200

- Max. blank / Workpiece Ø  	: 4.450

- Max. sheet thickness St 37	:  12 mm

- Centre distance upper bed out  :  2.000

- Longitudinal slide travel		: 2.100

- Lateral slide travel		:   500

- Spindle speeds range		: 2 – 300

- Spindle head stock		: DIN 15

- Spindle power			: 75 kW

- Stroke pinole			: 1.000

- Pressing force			: 20.000 Kg

- Total weight			: 35.000 Kg

Hydraulic Heavy/Duty spinning machine:

This machine is made up two separate parts which creates a large machining space capable of accommodating blanks up to 3300 mm in diameter. Cross slide and tailstock are hydraulically controlled. The upper bed can also be shifted hydraulically. All functions are easily controlled via control valves from a swivelling pendant control panel.

Please Note: The above information has been obtained to the best of our ability and belief from, and from the manufacturers where possible. It is given in good faith, but its accuracy can not be guaranteed. Accordingly, it will not form a representation or constitute contractual terms. We advise you to check any vital details !

Field of application of the machine:

Field off application of the machine; Tank ends, silo tunnels, fume hoods, rocket and prime mover components, large containers and flanged & profiled parts for tanks, vessels for the chemical and the aircraft industry.

# Text boxes

Transito 21

6909 DA BABBERICH Netherlands

Tel. +31 (0)316-247123

Fax: +31 (0)316-247956

info@mach4metal.com

www.mach4metal.com

Bank No : 66.52.13.883

IBAN    : NL33 INGB 0665 2138 83

BIC      : INGBNL2A